## Slide 1
Daniel Kleschew, Prof. Ulrich Nieken
8-10 September 2025, Lisbon/Portugal
15th European Congress of Chemical Engineering (ECCE)
Electrically Heated Ceramic Composite Tubes for Dry Reforming of Methane

## Slide 2: Electrification of Chemical Processes
Joule Heating
Heating - Meander
Multilayer Ceramic Composite Tubes [1]
Oxid Ceramic Matrix Composites
[1] Kolios, Grigorios, et al. (BASF SE) "Gas-tight, heat-permeable multilayer ceramic composite tube." U.S. Patent No. 10,865,151. 15 Dec. 2020

## Slide 3: Experimental Setup
Reactor Concept
CH4 + CO2
Heated reaction zone
Heat recovery
H2 + CO
Tube-In-Tube Design
Local heat release by metallic heater
40 mm
70 mm
Reaction
Heat exchanger
Reactants
Products
Counter-Flow Concept:
Heat recovery through counter-flow system
Educts are preheated by products in the opposite direction
Monolithic Ceramic Outer tube
OCMC Hybrid Tube

## Slide 4: Heating Behavior
Max.1150 °C
2.5 l/min
100 vol.% N2
Process conditions
Temperatures up to 1150 °C achievable
Targeted heat input through heat conductor design
Electrically heated zone
1200 W
2.45 Ω
54 V
22 A
Simulation:
Comsol with Bayesian Optimization

## Slide 5: Why do we need high Temperatures?
Dry Reforming.:
Reverse Water-Gas Shift Reaction:
𝐶𝑂2 + 𝐻2 ⇋ 𝐶𝑂 + 𝐻2𝑂
Soot Formation:
Boudouard Equilibrium:
Methane Decomposition:
Thermodynamic equilibrium @1 bar
High temperature improves conversion and minimizes soot formation

## Slide 6: Proof of Concept: Dry Reforming with Electrically Heated OCMC-Tube
Max.1150 °C
2.5 l/min
20 vol.% CH4
20 vol.% CO2
No Catalyst
Controlled process conditions
Sufficient heating in an inert atmosphere
Guaranteed prevention of soot formation Electrically heated zone
Successful proof of concept demonstrated
Conversion increases with temperature
Maximum conversion 72% at 1100 °C
Temperature [°C]
Conversion [%]

## Slide 7
Böblinger Straße 78
70199 Stuttgart
Daniel Kleschew
85309
Institut für chemische Verfahrenstechnik
daniel.kleschew@icvt.uni-stuttgart.de
Thank you for your attention!
Special thanks to:
PAPER